Flashback Configuration for Proxim AP-700 Wireless Access Point

Connecting to the Wireless Access Point:

● Launch your browser and in the address bar, enter the WAP's current IP Address as follows:

"http://192.168.10.XX"

● Press [Enter]

● When the Login prompt appears, enter the WAP password which appears of the Flashback configuration sheet (No user name exists)

● Click [OK] or press [Enter]

● Click the [Configure] button on the left

Within the Network tab:

● IP Address Assignment Type: Static

● IP Address: IP Address of WAP

● Subnet Mask: Subnet Mask for WAP IP Address

● Gateway IP Address: 192.168.10.10

● Click [OK] at the bottom to save

Within the Interfaces tab:

Operational Mode sub-tab: Wireless-A

● Operational Mode: "802.11g"

Wireless sub-tab:

● Network Name (SSID): SSID listed on Flashback configuration sheet

● Frequency Channel: Change if using multiple access points

● Load Balancing Max Clients: Change only if necessary

● Click [OK] at the bottom to save

Within the "SSID/VLAN/Security" tab:

Security Profile sub-tab:

Note: Edit existing profile or add a new one, if necessary…

● Checkmark either [Non-Secure] or [WEP Station] as needed to match DVR

● For [WEP Station], enter the WEP Key of DVR in all boxes

● Click [OK] at bottom to save

Wireless sub-tab:

Note: You can also edit your security profile's SSID from here

● Click the [Reboot] link on the left of the screen

● Click on the [Reboot] link in the following page to commit your settings

● Exit your browser and wait for the WAP to finish rebooting

(This takes about 1 minute)